## Slide 1
CASCA
SmartFit QC
Final Presentation
March 31st, 2021

## Slide 2
Project Refresher
Notes: Alex

## Slide 3
Perform quantitative quality control
Develop and build an autonomous quality control rig
Project Objectives
Integrate with Casca’s internal systems and databases
Notes: Alex

## Slide 4
Casca Production Process Overview
Customer orders insole
Fitter custom fits insole to foot scan
Insole is printed
Visual quality control
Quantitative quality control
Top sheet is glued
Top sheet is trimmed
Insole is shipped
Notes: Alex

## Slide 5
(New) Quality Control Process Overview
Read the QR Code
Fetch insole data
Perform Quantitative Analysis*
Compare to expected values
Update Database
Display results
* The quantitative analysis contains many quantitative visual and physical tests. These include compression testing, size validation, profile validation and weight validation. They will be discussed later in the presentation
Notes: Alex

## Slide 6
Rig Structure and Sensors

## Slide 7
Mechanical Design
Aluminum Extrusion Frame
Allows for weight savings and easy reproducibility
Polycarbonate Sheet Bed
Allows for color choice and easy manufacturing/mounting
Rail & Belt Bed Movement
Allows for smooth, silent, and precise movement
Touch Screen Control
Allows for customization of UI and ease of operation
Centering Guides
Allows consistent centering of insole
DC Driving Motors
Allows for precise and simple control
Notes: Mandy

## Slide 8
Mounted Sensors
Weight Measuring Load Cells
4 load cells mounted in a Wheatstone circuit allow to measure the weight of the insole
Length Measuring Camera
Allows measurement of the insole length using pixel per length ratio
ToF Sensors Array
Allows for the measurement of arch height at specific coordinates
Linear Actuator
Compresses the heel to test for under extrusion
Notes: Mandy

## Slide 9
Validation Solutions

## Slide 10
Length Validation Logic
Obtaining the sole length from a picture frame (OpenCV)
Bottom of the frame is a known distance away from the heel block
Finds the length of the insole in the frame of the picture by finding the last pixels of the sole color
Measured
Known
This requires the insole and the bed to have different colored surfaces
The measured length is then compared to the expected length from the database fetch
Notes: Beni

## Slide 11
(NEW) Orientation Validation Logic
Retrieve insole data API returns the orientation of a specific insole (L/R)
Determines whether the insole is a left or right depending on the largest distance from centerline
The outside of the sole will always have the largest measurement from the centerline
API Fetch
OpenCV Algorithm
Notes: Beni

## Slide 12
Weight Validation Logic
Extruded Volume
Volume to Weight
Theoretical
Experimental
1
2
1
2
The extruded volume is fetched from the database using the APIs
The weight of the insole is calculated by multiplying the volume of the print by the density of TPU
Measured Weight
The weight of the real insole is measured using the load cells mounted on the rig. The load cells act as a scale and their output is converted to a weight.
The strain in the load cell from an applied force produces an electrical resistance . When the 4 load cells are connected in a Wheatstone circuit, the total weight can be determined by measuring the voltage across the cells and converting it to a weight.
Notes: Johnson

## Slide 13
Compression Validation Logic
The experimental set of results will be conceived with the rig when it is complete and will correlate the applied force on the heel at a specific displacement with respect to the street size of the insole.
Compression Algorithm
A linear actuator is used to get a compression reading at the heel of the sole
An average of 50 readings are used to account for variability in results
The compression occurs at a fixed displacement. The force applied is then measured
Validation Algorithm
The mean force is compared to an experimental set of results and has to be correct within a certain margin of error
Notes: Johnson

## Slide 14
Theoretical
Arch Profile Validation Logic
Position of ToF sensors known with respect to the heel and centerline of the insole
ToF sensors obtain height measurements at the known coordinates
Using an .STL python library, able to calculate the surface height at the same coordinates as the ToF sensors
Time of Flight Sensors
Python .STL Library
The ToF sensors can remain in place as the insole is guaranteed to be centered due to the included centering guides
vs.
Experimental
Notes: Mandy

## Slide 15
Architecture and UI

## Slide 16
Project Architecture
Quality Control Rig
Databases
3D Printers
API Library
Print jobs and status’
Buckets
Data
Raspberry Pi
Arduino
REST APIs
Scale
Camera
TOF Sensors
Actuator
Bed Movement
Control Screen
Computations
Rig Actuation
Process Control
Notes: Karl

## Slide 17
Control Screen User Interface
Start screen possesses options for the testing type
Scanning screen shows a live feed from the scanning camera
Confirmation screen as for user confirmation of the sole details
During QC, progress is shown with the above progress bar
The result of the test is shown after completion
Additional information can be displayed at the user’s request
Notes: Beni

## Slide 18
Leveraged Technology
Hardware
Programming languages
Database tools
Python packages
Notes: Beni